## Slide 1: Heat flow from surface, and heat mining. concepts, evidence etc.
The Coal Authority
December 2019

## Slide 2
Temperature
Depth
10C
14C
Observations (approx. only) at Brains Brewery borehole, Cardiff, courtesy of Gareth Farr, BGS
75m
Expected T gradient
Actual T gradient
Observations show:
Actual T warmer than expected until ~75m
Warm surface T (“urban heat island” effect)
Negative T gradient implying:
Conductive heat flow downwards from surface to 75m
The negative gradient is similar to the usual positive geothermal gradient – implying that the flow of heat downwards could be around 70mW/m2
Evidence

## Slide 3
Temperature
Depth
0C
10C
200m
4C
Concept – heat conduction from surface
T gradient =
-3K/100m
T gradient =
+3K/100m
Abstraction point
Heat Flux upwards
~70mW/m2
Geothermal
Heat Flux downwards
~70mW/m2
Induced from surface
Heat Flux total
~140mW/m2
Suggested concept to maximise sustained heat flow to abstraction point by conduction (ie ignores heat advection).
Concept suggests gradients developed for long term steady state. ie after a period of heat mining to move away from the natural geotherm.
Represents annualised average values – seasonal differences could occur
Represents spatially averaged values – colder eg by 5K at injection than abstraction
For mine water flow based schemes, advection would cease if freezing occurs (T < 0C). Also flow from injection to abstraction would cease, hence stopping operation.

## Slide 4
Concept - variants
Abstraction at 100m
With steady state T = 4C
This would give double the conductive heat flux from surface- ie ~140 mW/m2
Hence total sustainable heat =
140 (surface) + 70 (geothermal) = 210 mW/m2
Note:
1 mW/m2 = 1kW/km2

## Slide 5
Temperature
Depth
Concept – Heat advection by recharge
T gradient =
+3K/100m
Abstraction point
Heat Flux upwards
~70mW/m2
Geothermal
Advected Heat Flux (Recharge) downwards
~70mW/m2
from surface
Heat Flux total
~140mW/m2
Assume rainfall recharges ground at 100mm/yr, and this recharge is sufficient to extract heat energy, equivalent to dT =5K.
Flow/Area = 100mm/yr = 100L/yr/m2
= 3E-6 L/s/m2 = 3L/s/km2
Using 4200 J/kg/K, with dT = 5k, gives
Heat flux = 67mW/m2 (advected by recharge)
So the estimated advective heat flux in recharge water is similar to the geothermal flux (both approx. 70 mW/m2)
Unclear if conduction of heat could also be induced from surface whilst recharge is advecting heat vertically down?
Depth of such advective heat transport will depend how deep the recharge circulates in ground
Recharge
100mm/yr

## Slide 6
Questions arising
For various depths (in mines) what is relative steady state ratio of induced surface heat conduction flux to geothermal flux?
And is there a depth at which induced surface heat conduction becomes impractical?, or insignificant?
Below what depth does advection of heat from surface (ie recharge) become important?
Does advective recharge heat flux deduct from, or add to, the induced conductive heat flux from surface?

## Slide 7
The Environment Agency’s approach to groundwater protection February 2018 …
Ground source heating and cooling (GSHC) systems utilise a renewable energy source, namely the warming of the ground by solar radiation that keeps ‘shallow’ groundwater at its constant temperature. Heat from deep in the Earth’s interior can also warm groundwater, but this is not normally significant within 100 metres of the surface. For the purposes of these position statements, any schemes that use heat from the Earth’s interior will be called ‘deep geothermal schemes’ and not GSHC systems.
Reference

## Slide 8
Concept – Heat Mining estimated duration
Heat extraction will cause Temperatures to fall.
Falling temperatures will continue until steady state is achieved.
The rate of temperature decrease will in theory be most rapid at the start of heat extraction, and subsequently will slow down – until steady state is eventually reached.
The period of non-steady state heat extraction is removing heat from storage, and may therefore be called heat mining.
Note the above behaviour has a direct analogy with groundwater level trends after pumping begins, and with the eventual forming a steady state cone of depression
Take a 1m depth of stored ground water.
Temperature Decrease of 5K equates to
Energy extracted = 21MJ/m2
For heat extraction rate of 70mW/m2, equal to geothermal flux,
Heat energy extraction takes 9.5 years.
Note that this simple estimate ignores heat stored in the rocks – This additional stored heat (if extractable) would extend the period of heat mining.
As an initial approximation 1m water depth can be considered typical value for each worked seam. This assumes a seam extraction thickness of 2m, and a residual void fraction of 50%.

## Slide 9
 | 0.1 km2 | 0.5 km2 | 1 km2 | 5 km2 | 10 km2
50 kW | 1.3 y (500 mW/m2) | 6.6 y (100 mW/m2) | 13 y (50 mW/m2) | 66 y (10 mW/m2) | 130 y (5 mW/m2)
100 kW | 0.66 y (1000 mW/m2) | 3.3 y (200 mW/m2) | 6.6 y (100 mW/m2) | 33 y (20 mW/m2) | 66 y (10 mW/m2)
500 kW | 0.13 y (5000 mW/m2) | 0.66 y (1000 mW/m2) | 1.3 y (500 mW/m2) | 6.6 y (100 mW/m2) | 13 y (50 mW/m2)
1 MW | 0.066 y (10,000 mW/m2) | 0.33 y (2000 mW/m2) | 0.66 y (1000 mW/m2) | 3.3 y (200 mW/m2) | 6.6 y (100 mW/m2)
5 MW | 0.013 y (50,000 mW/m2) | 0.066 y (10,000 mW/m2) | 0.13 y (5000 mW/m2) | 0.66 y (1000 mW/m2) | 1.3 y (500 mW/m2)
Nominal period of time (years) over which heat can be mined from 1m depth of groundwater – for varying catchment size (km2), and net-heat extraction rate (kW)
catchment size (km2)
net-heat extraction rate
(kW, as annual average)
Notes – To account for different depths of groundwater containing heat, multiply the number of years by the depth eg if 5m of water depth, multiply no. years by 5.
- heat stored in rock matrix around groundwater is NOT included. Including this would extend the timescales.