## Slide 1: Tongonan geothermal reservoir, Philippines Di Rienzo D.I., Dirscherl M., Preine J., Receveur M., Repczynska M.M.
Location:
In central highlands of Leyte province/island (Eastern Visayas region)
Geological Setting:
Within tectonically active Philippine Mobile Belt
  Eastern bound: Philippine Trench
  Western bound: Manila Trench, Negros Trench, Cotabato Trench
  Philippine Fault Zone (NW-SE)
  Hosted by andesitic volcano-sedimentary units intruded by microdioritic dykes
  Size:
  One of largest water-dominated systems in the world
  2 hydrothermal systems in Leyte Geothermal Production Field: Tongonan, Mahanagdong
  Production sectors Tongonan (15 km2): Upper Mahiao, Tongonan-1, Malitbog, South Sambaloran
  Reservoir characteristics:
  Stored heat capacity Tongonan: 590-740 MW
  Convective upflow centered in area of Upper Mahiao and Tongonan-1
  Lateral outflow toward Malitbog and UM
  Up to 300°C (relatively constant over time, mostly 280°C contour)
  Fluid enthalpy : 1500-2700 kj/kg
  Current exploitation and management strategies:
  Exploration since 1960’s
  Commercial operation since 1983: Increased production over time led to changes in reservoir response
  Adaption strategies
  LGPF provides 37 % installed geothermal capacity in Philippines
  3 power plants – Total installed capacity: 710 MW
  Total mass extraction rate: 5Mt/month - Total brine injection rate: 2 Mt/month (2000)
References: Uribe et al., 2015; Dacillo et al., 2010; Ana et al., 1999; Austria et al., 2015; Mismanos and Vasquez, 2015.
Notes: changes in reservoir respond (e.g. pressure , -> increased discharge enthalpie,s boiling central production field -> two-phase regions (steam), cooler water inflow)
  (Subduction Philippine Sea Plate under PMB)
  (Subduction Sunda Plate under PMB))
  New strategies developed (e.g. interconnection steam lines, well workovers, steam production)
changes in reservoir respond (e.g. pressure ↓, increased discharge enthalpies -> boiling central production field -> two-phase regions (steam↑), BUT then pressure ↓, cooler water inflow -> steam reduced again)