## Slide 1: Site visits

## Slide 2: A winning treatment site

## Slide 3: Field Work: Dipping

## Slide 4: Durham area
Horden
Dawdon
Easington
Minewater flow
Minewater flow
River Wear
Ludworth Dyke

## Slide 5
Dawdon

## Slide 6: Dawdon shaft
Theresa shaft (about 300 m depth), capped but not overfilled. Water about 50 mBGL (20 mBSL)
Pumping started in 2008
Two pumps (about 100 mBGL or mBSL?) + Gas vents to allow degassing (no methane released anymore as Coal Measures are flooded).
Curved horizontal pipe is rejecting treated mine water into the sea.
20degC minewater used to heat treatment plant (heat pump).

## Slide 8: Dawdon treatment plant
Active treatment plant (150 L/s capacity but only pumping 80L/s) – Passive treatment with reed beds not possible due to hypersaline minewater.
Treatment scheme composed of 3 sets of 4 tanks in series, running in parallel:
  1st tank: stirring for degassing 20 degC water
  2nd tank (1st reactor): large iron sludge forms – pHmeter
  3rd tank: (2nd reactor): increase pH by injecting limewater
  Decantation ponds: forms polymer where finer iron precipitates forms and decant rapidly – reinjected into 1st reactor. Overlying sludge goes to filter press.
  Clean water reinjected into ocean. About 20-25 tons of iron sludge / month?
Blower Room
Transformers, Panels and Control Room
Workshop/lab
Lime Silo
Sludge Thickening and Disposal
(Filter-press)
Clarifier
Clarifier
Clarifier
Stage 2 Reactor
Stage 2 Reactor
Stage 2 Reactor
Sludge Holding Tank
Stage 1 Reactor
Stage 1 Reactor
Stage 1 Reactor
Sludge Holding Tank
De-Gassing Tank
De-Gassing Tank
De-Gassing Tank
Polymer
Make-up Area
Mixed Lime Holding Tank
Lime Mixing Tanks
Outlet
Tank
Process water stock

## Slide 11: Dawdon treatment plant
Built in addition of the Horden facility because fault/dyke separating the mines (dammed). Opened dam might connect the two mines as pumping at Horden (from 2004) has been detected at Dawdon.
Pumping commenced August 2004

## Slide 12: Horden
Horden shaft – shallower than at Dawdon.
Only one pump
Reinject water into the sea using similar curved pipe.
Pumping started in 2004 (active plant)
Quality of water decrease if pumped harder (salinity and Fe increase)

## Slide 13: Horden
Originally a temporary active treatment plant (100 – 50 L/s) replaced by a passive treatment plant (capacity 50 L/s) in 2011 after Dawdon started.
2 settlement lagoons in parallel, 2 reed beds in series
Small reed beds due to salinity of water – not well developed in second reed bed as used with original plant (higher salinity).
Calcite precipitate in cascade?

## Slide 14: Horden

## Slide 15: Easington

## Slide 16: Seaton Sluice upwelling
Underlying workings (Bates area)
Adit connects to the river

## Slide 17: Lynemouth
Composed of two phases:
  Phase 1: two lagoons in series
  Phase 2: two series of 3 and 2 lagoons running in parallel.
  Both discharged to the sea

## Slide 18: Lynemouth - Phase 1

## Slide 19: Lynemouth - Phase 2

## Slide 20: Lynemouth
‘Greenhouse’ dry ochre

## Slide 21: Meeting report
Modeling
  Start with simple models to identify which features of the mines are important to determine the temperature of water when reaches the abstraction point :
    mine shafts / roadways / longwall panels
    vertical/lateral geometry, volume of workings, presence of diping coal seams bringing water down from surface
    depth of production…
When looking at mine plans, identify:
  Are workings well connected to main flow path?
  Connection between mines
  Connection between seams
Type of model:
  2D models – steady state model – ??
  Simulation of heat extraction
  Identification of zone of influence
  At what rate water is cooling down at the surface / heating when going down?
Notes:
  Shallow workings are the wettest (recharge from rainfall), deeper seams doesn’t not respond as much from rainfall so less inflow

## Slide 22: Long – term objectives
Bilston Glen
  Simple 2D model of Bilston Glen
  How can existing digital GIS data be used in the model?
  What are the limitation of the available data?
  Identify flow path from mine plans and make sure that they are represented in the simulations
  Are lateral panels around roadways important?
Dawdon
  Mine flooded in 10-15 years
  Pumped water temperature 20C since 11 years at a rate of 80 L/s
  Which water flooded the mine?
  5 T-depth profiles from dawdon/harden before/after pumping
Data required:
  Data about rock temperature in the mine (historical data to plan ventilation)
  Temperature profile in borehole/wells (no turbulent flow)