## Slide 1: Units of Measurement for Hydrogeology
Knowledge Transfer

## Slide 2: Aims
This document aims to summarise important, and common units of measurement.
Which are used by the hydrogeologist working on mines.
Common conversions between units, e.g. metric and imperial are given

## Slide 3: Contents
Levels, Elevations, Depth
Gradients, Angles
Pressure
Volume
Flow
Concentrations of Gas
Chemistry
Energy and Power

## Slide 4: Levels and Elevations
mAOD – meters Above Ordnance Datum
  Height above sea level
    Alternative
    mOD
    mASL (Above Sea Level )
Negative values, below OD, e.g.:
    -30 m AOD, or
    30 m BOD (Below OD)

## Slide 5: Depth
mBGL – meters Below Ground Level
  Alternatives include
    mBSL - Below Surface Level
    mBDat – Below Datum
    mBTOC – Below top of casing
    mBEFL – Below Enginehouse floor level
    etc
  Key point is to understand what reference point (datum) is being measured to.

## Slide 6: Mine plans – most modern, metric
Since many modern workings are below sea level, to avoid always including the minus symbol (possible confusion with other dashes) convention can be to only label “+”values
    200 = -200 mAOD = 200m BOD
    +200 = 200 mAOD
    Sometimes [ ] placed around values to clearly differentiate +ve values

## Slide 7: Mine plans – most modern, metric

## Slide 8: Mine plans – modern, non metric
Commonly use a MINING DATUM
10,000 feet below OD is most common
  3048mBOD = 3kmBOD
  Cf deepest UK mines ~1km, so avoids negatives
  CHECK mine plan legend as others were used

## Slide 9: Mine plans – modern, non metric
Two step conversion to mOD
  Eg1 : 10,050’AMD (Above Mining Datum).
    Datum change : 10,050’ – 10,000’ = 50’AOD
    Units change : 50’AOD = 15.2mAOD
  Eg2 : 9,775’AMD.
    Datum change : 9,775’ – 10,000’ = -225’AOD
    Units change : -225’AOD = -68.6mAOD = 68.6mBOD

## Slide 10: Mine plans – modern, non metric
Depth given in yards – not feet
Accurate elevations use feet with decimal places (not fractions)
Contrasts with use of feet and inches for fault throws e.g.
1/6 = 1 foot 6 inches, or
1/- = 1 foot 0 inch,
and seam sections e.g.
4’7” = 4 feet 7 inches

## Slide 11: Old mine plans
Fathoms, chains, etc
1 foot (1’) = 12 inches (12”)
1 yard = 3 feet
1 fathom = 2 yards = 6 feet (normally)
1 chain =22 yards

## Slide 12: Opencast surface mine plans
Often use a bespoke Site Datum
  Avoids dealing with –ve levels when below OD
  Eg site datum 0 mSD = -100 mAOD
  Need to identify what site datum used:
    From legend of plans
    By comparing to OS contours on adjacent land

## Slide 13: Gradients
Mine infrastructure
  1 in 4 e.g. for a drift mine entrance + arrow down
  Avoid confusion with arrows for throws on faults!
  Flat (ie gradient = zero) often labelled “Level”
Geological Dip
  1 in 12 “full dip” annotated arrow pointing down
Hydraulic gradient (slope for water table)
  1 in 500
1 in # is very common,
  alternatives of using #%, or degrees are rare

## Slide 14
Example of a short “Level” section of cross measures road.
Level =
Flat / Horizontal

## Slide 16: Gradient - Angle conversion
1 in 10 gradient
Tan(a)=dy/dx = 1/10
a= tan-1(dy/dx) = tan-1(0.1) = 5.7o
  Phone calculator can do this
  Beware – Excel uses radians, so need to convert from degrees:
  Gradient dy/dx = TAN(RADIANS(a))
    If you input formula correctly, then dy/dx=1 for a=45o
  Angle a = DEGREES(ATAN(dy/dx))
dy
dx
Angle a

## Slide 17: Borehole angle
A borehole needs to hit a target:
100 m depth (dx)
Horizontal tolerance 1m (dy)
  Eg if aiming for centre of 2m wide roadway
dy/dx = 1/100 = 0.01
So max angle of deviation from vertical is:
a= tan-1(dy/dx) = tan-1(0.01) = 0.57o
dy
dx
Angle
a

## Slide 18: Pressure
Pressure can be measured in:
  Water (and other fluids)
  Gas (or more generally air)
  Rocks (or any solid material)
Pressure = Force / Area
[Pascal] = [Newton] / [m2]
1 Pa = 1 N/m2 = 1 kg/m/s2

## Slide 19: Pressure - Water
Piezometric Pressure :
Pressure = Force / Area = Mass.gravity/Area
  Multiply top & bottom by depth (h)
Pressure = Mass.gravity.depth/Volume
Pressure = Density.gravity.depth
P = Dgh
units [Pa] = [kg/m3].[m/s2].[m]
Normally pressure is expressed as head of water in meters; but if saline water is present then calculating actual pressure may be useful

## Slide 20: Pressure
Alternatives to Pa, kPa, Mpa, include:
Bar
  1 bar = 100,000Pa = 100kPa = 105Pa
  1 millibar, mb = 100Pa
m H20; meters head/depth of water
  10 meters water column depth ~ 1 bar
    Accurately 10m H20 = 0.98 bar
cm H20 (eg some pressure sensor loggers)
  1 cm H20 = ~1mb = ~100 Pa

## Slide 21: Pressure
Atmosphere (ie typical atmospheric pressure)
  1 atm = 1.013 bar (and ~10m H2O)
PSI pound per square inch
  14.5 psi = 1 bar
mm Hg, millimeters of mercury (rare nowadays)
  1 mmHg = 133 Pa

## Slide 22: Volume - metric
1000 Litres = 1 m3
1 ML, megalitre = 1000 m3
1 Litre = 1000 cc (cubic centimeters / cm3)

## Slide 23: Volume - imperial
Gallons
  A UK, or Imperial gallon is ~20% bigger than US gallon, so avoid using US (American) units
    Googles converter includes both
  1 gallon = 4.55 litres
  1 litre = 0.22 gallons
  1 m3 = 220 gallons

## Slide 24: Flow rates - metric
Flow = Volume / Time
L/s Litres per Second – our usual preference
Alternatives
  m3/s, or “cumecs”; cubic meters per second
  m3/hr
  m3/day
  ML/d megalitres per day

## Slide 25: Flow rates – metric conversions
Convert to L/s | Conversion factor
1 m3/s = 1000 L/s | x1000
1 m3/hr = 0.28 L/s | x1000/60/60 = /3.6
1 m3/day = 0.012 L/s | x1000/60/60/24 = /86.4
1 ML/d = 11.6 L/s | x1000,000/60/60/24 = x11.6

## Slide 26: Flow rates - imperial
Gpm = gallons per minute was common
1 gpm = 0.076 L/s (convert divide by 13.2)
1 L/s = 13.2 gpm
  Occasionally see
    gph, gallons per hour
    gpd, gallons per day

## Slide 27: Pumping v Abstraction Rates
Take care to differentiate these similar rates
Pumping rate = instantaneous rate at which flow is delivered by pump
  Usual unit = L/s
Abstraction rate = total abstracted (ie pumped) over given time interval (eg 1 day, 1 week etc)
  Usual unit = L/s
OR
Abstraction Rate = averaged pumping rate

## Slide 28: Pumping v Abstraction Rates
Example – Pump runs at 10 L/s for 12 hrs/day, and is OFF (0 L/s) for 12 hrs per day.
Pumping rate may be recorded as either 0, or 10, depending when the visit occurs in pumping cycle.
Abstraction rate = 10x12/24 = 5 L/s
In practice, pumping rate often > abstraction rate
Note its more accurate to calculate abstraction from volume totalisers, as opposed to estimating using the pumping rate and the hours run totaliser.
Take care with multiple pumps, or totalisers
  Different combinations exist

## Slide 29: Concentrations - Gas
Can be as ratio of either :
Constituent Volume / total Volume
  %v/v (most common; dimensionless)
Constituent Mass / total Volume
  mg/L
  %w/v where w indicates weight, or mass
For concentrations below the % range:
  ppt part per thousand; 1ppt = 0.1%v/v
  ppm part per million; 1ppm
  ppb part per billion; 1ppb

## Slide 30: Concentrations – Methane gas
Normally recorded as
  %v/v
But, some instruments report methane relative to explosive range; eg:
  % CH4 LEL (methane Lower Explosive Limit)
  % CH4 UEL (methane Upper Explosive Limit)
LEL is ~5% CH4 v/v
UEL is ~15% CH4 v/v
Best check instrument instructions to convert from LEL / UEL type readings

## Slide 31: Concentrations – Dissolved gas
For testing of dissolved gas take care if the result is reported in the fluid itself, or in an equilibrated headspace above the fluid.
Example units:
  mg/L
  ccSTP/L -cm3 @ Standard Temperature +Pressure

## Slide 32: Chemistry
Concentrations
Loading
Electrical Conductivity
Alkalinity

## Slide 33: Concentrations - Water
Concentration = Mass / Volume
mg/L milligram per litre
ug/L microgram per litre: “u” is Greek “mu”
1000 ug/L = 1 mg/L
Sometimes expressed as
  ppb part per billion; 1ppb = 1ug/L
  ppm part per million; 1ppm = 1mg/L
  ppt part per thousand; 1ppt = 1g/L
  Above assumes 1 litre fluid has mass 1kg =1000g

## Slide 34: Loading (of chemicals in flowing water)
Loading = Concentration x Flow = Mass / Time
E.g. mg/L x L/s = mg/s
Typical alternative units:
  Kg/day
  Tonne/year

## Slide 35: Electrical Conductivity
Siemens per meter, S/m – SI unit
uS/cm is far more common unit in practice
CARE needed for:
uS/cm OR mS/cm ???
  Micro units most common in aquatic freshwaters
  Milli units can indicate saline waters
Temperature normalised?
  EC increases with fluid temperature
  Normalise to 25oC as common reference temperature (nominally “room temperature”)

## Slide 36: Electrical Conductivity
Best to state the temperature; e.g.
  450 uS/cm @25oC
Historically 20oC may have been used!
EC can also be called Specific Conductance, SC,
For geophysical logging of boreholes often both actual EC, and normalised EC recorded – be clear which!
Rule of thumb, each 1oC increase gives 2% increase in EC value. So
  Actual water temperature of 15oC
  EC =1000 uS/cm;
  so add (25-15)x2%= 20% to give
  EC = 1200 us/cm@25oC

## Slide 37: EC and TDS
Most meters measuring EC will also convert this to Total Dissolved Solids, TDS.
Straightforward for fresh waters, as it’s a linear relationship,
  Eg 1000uS/cm = 640 ppm TDS
But becomes non linear as salinity increases.
Typically EC with units of
  uS/cm EC converts to ppm TDS
  mS/cm EC converts to ppt TDS

## Slide 38: Alkalinity
mg/l as CaCO3 – most common units
  The as ??? Is important as it tells you what Alk is when expressed in the equivalent mass of the specified substance
Alkalinity is a concept; not a molecule
  Alk = 2CO32- + HCO3- + OH- - H+ [each as mol/l)
    Alk = carbonate + bicarbonate + hydroxide – protons
    Carbonate ion concentration is doubled due to charge of 2
  “Net-Alkalinity” is a different concept, normally relating the alkalinity to the acidity potentially generated from metals

## Slide 39: Alkalinity
Can express Alk in charge equivalents (eq)
1meq/l = 50 mg/l as CaCO3
Occasionally may see eg “carbonate alkalinity”
60 mg/l as CO3 = 100 mg/l as CaCO3
  By calculating molecular masses:
  CaCO3 = 40 +12 + 3x16 = 40 + 60 = 100

## Slide 40: Alkalinity
Measurement in practice (field / lab):
Alkalinity – titrate sample with acid to endpoint, normally at pH=4.5
Acidity– titrate sample with alkali to endpoint, normally at pH=8.3 (variants: cold, hot, peroxide)

## Slide 41: Temperature
Degrees Celcius °C
  The SI unit
  Centigrade is old fashioned name for same scale
  Water freezes at 0 °C and boils at 100 °C
Kelvin
  Same size as Celsius ; 1 K = 1 °C
  Scale starts at absolute zero; 0K = -273.15 °C
Degrees Fahrenheit °F
  Used in America

## Slide 42: Energy and Power
Mechanical (lifting water)
Electrical (running pumps)
Heat (geothermal energy

## Slide 43: Energy and Power - General
Energy (Work done) = Force x Distance
Energy SI unit = Joule
  kJ, or MJ common
Power = Energy/ Time (rate of use of energy)
  Power SI Unit = Watt
  1 Watt = 1 Joule/second
    1kW = 1 kJ/s = 1000 J/s
Energy = Power x Time

## Slide 44: Energy and Power - Mechanical
To move water up (or down)
Energy = Force x Distance
Energy = mass x gravity x height (i.e. mgh)
[J] = [kg] x [m/s2] x [m]
Often called Potential Energy, PE
  Hydropower turbines convert PE into electric energy (the opposite of pumps)

## Slide 45: Energy and Power - Mechanical
Power needed to lift a steady flow Q of water
Power = Energy/ Time
Power = mgh/t = (m/t).gh
Since flow Q = V/t and density D = m/V
  DQ = m/t
Power = D.Q.gh
[W] = [kg/m3].[m3/s].[m/s2].[m]
Or [W] = [kg/L].[L/s].[m/s2].[m]
  So for fresh water density 1kg/L, Power = Qgh
  9.8W needed to lift 1L/s by 1m

## Slide 46: Energy and Power - Electrical
Energy = Power x Time
Hence kiloWatt-hours, kWh common
  1 kWh = 1000x60x60 = 3.6MJ
Avoid confusing kW with kWh ! ( common!)
Calculate electrical power by
  Power = Voltage . Ampage(current) [VA]
But beware power supplies are rated as kVA, but due to efficiency factors kVA is similar but not identical to kW!

## Slide 47: Energy and Power - Heat
Heat extractable from a substance depends on
  specific heat capacity, c, of substance
    For water, c= 4,200 J/kg/°C
  change in temperature dT (in °C, or K, Kelvin)
Energy = c.mass.dT
[J] = [J/kg/°C]. [kg].[°C]
So lowering 1kg water by 5°C provides:
Heat energy = 4200x1x5 = 21,000J = 21kJ
  Converts to 6Wh; equivalent to running an energy efficient 6Watt light bulb for an hour

## Slide 48: Energy and Power - Heat
Other units for heat energy, include:
Calories
  1 calorie = 4.2 J
British Thermal Units
  1 btu = 1055 J

## Slide 49: Energy and Power - Heat
Power = Energy/ Time
Power = c.mass.dT / Time = (m/t).c.dT
Since flow Q = V/t and density D = m/V
    D.Q = m/t
  Power = D.Q.c.dT
  [W] = [kg/m3].[m3/s] [J/kg/°C].[°C] = [J/s]
Or [W] = [kg/L].[L/s] [J/kg/°C].[°C]
  So for fresh water density 1kg/L, Power = Q.c.dT
  Power = 1 x 4200 x 5 = 21,000 W
  21kW released from 1L/s with a 5oC change