## Slide 1: Model notes

## Slide 2: Hydrological model
2D/3D numerical model based on a lumped-parameter model approach, using
  Exact location of the discharge
  Representation of the flow path (i.e. sloping strata, roadways, shafts)
  Include boundary conditions (i.e. lateral + source/sink terms)
  Hydraulic parameters for each system feature (i.e. ‘ponds’)
  Turbulent flow using pipe network model for larger flow pathways superimposed to aquifer (i.e. VSS) model to model interactions between aquifer (intact strata) and conduits in mined out areas.
Inputs:
  Precipitation/evaporation/transpiration
  Spring discharge / well abstraction
  Stream-aquifer interaction
  Inflow from deeper aquifers / marine inflow / inflow from lateral ponds
Ouputs:
  Water balance (= recharge rate) and water level time-series
  Timing / volumetric flux of the surface discharge

## Slide 3: Hydrological model
Data:
  Groudwater levels
  Pumping rates
  Recharge rates
  Seam elevation and location of outcrops
  Strata type and thickness
  Location of workings / major roadways
  Boundary conditions (i.e. fixed head / flow)
  For aquifer model:
    Porosity
    Specific yield / storage
    Hydraulic conductivity
    Unsaturated zone parameters
  For pipe network:
    Pipe length, diameter, roughness
    Node elevation
    Location and elevation of fixed heads
Recharge rate : R=[P-ET-S]-SMDt

## Slide 4: Required data
Flooding data (water level TS / flow rates)
Pumping / abstraction rates

## Slide 5: Statistical analysis
Cross correlate temperature at each site (sort out by measurement type) with
  Geology
  Proximity of fault / dyke / granite
  Reharge rate

## Slide 6: Thermal model – Model set up
2D model
Worked area
  Porosity =
  with n the number of workings in the considered mine volume, A the working area and h the worked seam thickness.
Roadway: high conductivity pathway between mine volumes, representing connections between different mines and/or mined parts of a same mine (if large extent)
  Shafts
  Roadway

## Slide 7: Thermal model – Model set up
Required data
  Underground working shapefile:
    Area
    Seam thickness
    Depth min / depth max
    Dip
    Type (total / partial extraction)
    Colliery name
  Roadway
  Mine entries (shafts, staple shafts, adits)
Identify monitoring points and data available at those points (total time period and data type)
Identify all connections between surface discharges and underground workings

## Slide 8: Model set up
Merge corresponding working polygon
Extract points around shpefiles (X, Y)
Calculate depth at each points using dip
Import in gmsh
Calculate initial void volume at each point (sum of working layers vertically)
Calculate expected amount of subsidence
Determine residual void volume
Statistical distribution with depth
Output main workings
Connect each roadway to production/injection well
Determine initial and BC
Calibrate model with flooding TS / temperature prod and/or discharge flow rate

## Slide 16
Roslin
Ramsay
Burghlee
Bilston Glen
?
Shallow workings (Whithill, Polton, Glenesk, Eldindean, Dalhousie, Alkaiden…)
Discharge zones
Junkie’s
Bryan’s
Lady Victoria/
Lingerwood
Lingerwood/Easthouse
Arniston
Newton Grange
Newbattle
Victoria and
Dicken’s shafts
Emily’s shaft
?
?
Easthouse
incline/shaft
Bilston Glen shaft

## Slide 20: Thermal model – Model calibration
2D models natural state (no pumping)
i.e. Bilston Glen / Easthouse
Initial condition:
  Initial head at the end of mining
  Estimated temperature gradient from literature
Simulation of flooding (based on water level time series)
Boundary conditions :
  Thermal: constant surface/bottom temperature
  Water recharge: rainfall (+marine, aquifers, lateral mines)
Output
  Time series of water level / temperature
  Vertical profile in shafts / borehole of:
    Temperature
    Salinity (related to EC)
Compare simulated time-series and profiles with:
  Existing time series from discharge/monitoring points (i.e. shafts)
  EC-T logs in shafts/boreholes

## Slide 21: Thermal model – Model calibration
2D models natural state (no pumping)
i.e. Bilston Glen / Easthouses
Initial condition:
  Initial head at the end of mining
  Estimated temperature gradient from literature
Simulation of flooding (based on water level time series)
Boundary conditions :
  Thermal: constant surface/bottom temperature
  Water recharge: rainfall (+marine, aquifers, lateral mines)
Output
  Time series of water level / temperature
  Vertical profile in shafts / borehole of:
    Temperature
    Salinity (related to EC)
Compare simulated time-series and profiles with:
  Existing time series from discharge/monitoring points (i.e. shafts)
  EC-T logs in shafts/boreholes

## Slide 22: Thermal model – Model calibration
Data source:

## Slide 23: Thermal model – Model validation
Data covering PhD lifetime